Ken-Tool announces Valve Breaker™ tool

Quickly removes valve stems from rims

AKRON, Ohio (June 15, 2010) – Ken-Tool, the world’s leading manufacturer of professional tire service tools, has announced its latest tire service tool, the Valve Breaker™ to quickly remove valve stems from demounted wheels.

The patent pending Valve Breaker is compact and powerful; using a slide ram design to drive a heat-treated punch into the valve stem seat to easily pop the valve stem out of the rim after the wheel has been demounted.  This allows the service technician to quickly remove the stem with the wheel on the floor. The slide ram is made from solid round steel bar stock to drive more energy into the valve stem to knock it out of the wheel quickly and efficiently.

The Ken-Tool Valve Breaker protects the operator with a rubber safety-grip drive handle and a vibration absorbing rubber grip on the outer tube. A protective flange at the top of the tube helps to prevent pinching, and an energy absorbing spring loaded punch assembly protects the wheel while reducing shock to the operator’s hands.

The Valve Breaker is made in the U.S.A., and is available in two lengths: P/N 35934 – 27 in. (69 cm) and P/N 35936 – 45 in. (114 cm), and weigh 9 lb (4.1kg) and 16 lb. (7.3 kg) respectively. The shorter Valve Breaker (P/N 35934) fits conveniently in a 30” toolbox.

The Valve Breaker tool is easy to service, with three components needed to rebuild the tool – the punch, a spring and a roll pin.  A Repair Kit, P/N 35935, includes these replacement components.

NOTE: Please refer to the video demonstration at http://www.youtube.com/user/KenToolVideoMedia#p/a/u/0/dyx-OqN0QVU  to see how quickly and simply the Ken-Tool Valve Breaker removes the valve stem from a wheel.

Ken-Tool products are available through leading tire industry supply distributors worldwide.  For more information about these and other professional tire-changing tools, visit www.kentool.com. High resolution images of the Valve Breaker™ are available on line at http://www.kentool.com/kentoolmedia_images.html.

About Ken-Tool
Ken-Tool is the world’s leading manufacturer of professional tire service hand tools. Headquartered in Akron, Ohio, Ken-Tool has been providing the tire industry and automotive aftermarket with quality products for nearly 90 years.

Contact:

Rock Tyson, CME
VP. Sales &, Marketing
Ken-Tool 
768 E. North St.
Akron, OH  44305 
330-252-1957 office

Steve Cole

WRITEWords

635 Shaker Drive

Medina, OH 44256

330-725-5462

scole@4writewords.com