Ken-Tool adds to Truck Wrench line

Includes new plus improved products

AKRON, Ohio (March 6, 2012) – Ken-Tool, the leader in tire service tools, has announced a significant expansion of its double-ended truck wrench product line, with three all new products, and improvements to three current offerings.

The new wrenches are made from forged carbon steel for years of trouble-free service.  These wrenches are ideal for trucks, buses, agricultural and other on and off-the-highway equipment.  All the wrenches are approximately 16-inches (41 cm.) long, and use the Ken-Tool TR5 and the new TR5A hexagonal wrench handle.

| NEW ITEM # | MODEL # | SOCKET SIZES | APPLICATION |
| --- | --- | --- | --- |
| 32519 | TR99 | 33mm Hex w/ 13/16” sq X 1/2” Hex | SAE inner & outer Budd wheel nuts, plus hub piloted wheels |
| 32599 | TRM6A | 33mm w/ 21mm sq X 41mm Hex | Metric inner & outer Budd wheel nuts, plus hub piloted wheels |
| 32512 | TR2A | 1” Hex w/ 5/8” X 1-3/16” Hex | Caterpillar & Bobcat equipment and hub piloted wheels |
| 32319 | TR5A | 30” (76 cm) Truck Wrench Hex Handle | 8” (20 cm) longer than standard TR5 Truck Wrench Hex Handle, provides greater leverage |
| IMPROVED – Double-ended Wrenches with DEEPER SOCKETS (Fits longer wheel studs & lug bolts) Highlighted copy is the change. Original Item/Model numbers remain the same on improved wrenches. |
| 32506 | TR3X | 1-1/16” Hex X 1-3/16” Hex | 1-3/16” Hex socket – 1-3/4” (4.5 cm) Stud Depth |
| 32553 | TRM3 | 27mm Hex X 30mm Hex | 30mm Hex socket – 1-3/4” (4.5 cm) Stud Depth |
| 32557 | TRM7 | 30mm Hex X 33mm Hex | 30mm Hex socket – 1-3/4” (4.5 cm) Stud Depth |

Ken-Tool has also introduced the 34420 Heavy Duty Wheel Nut Removal Tool, which has become a standard item in military motor pools.  It features 700 ft-lbs of torque capability, and has an integral handle extension for greater leverage on stubborn nuts.

| ITEM # | MODEL # | Description | Application |
| --- | --- | --- | --- |
| 34420 | 34420 | Provides up to 700 ft-lbs (96.8 kg-m) of torque. Socket: 1-1/2”; Depth: 1-1/4” Length: 25.5” (65 cm); extended 44” (112 cm) | Wheel nut removal, w/ extra extended leverage handle; Original MIL-spec version |

See following page

Ken-Tool products are available through leading tire industry supply distributors worldwide.  For more information about these and other professional tire-changing tools, visit www.kentool.com. High resolution images are of the new wrenches and handles are available on line at http://www.kentool.com/kentoolmedia_images.html.

About Ken-Tool
Ken-Tool is the world’s leading manufacturer of professional tire service hand tools. Headquartered in Akron, Ohio, Ken-Tool has been providing the tire industry and automotive aftermarket with quality products for nearly 90 years.

Contact:

Rock Tyson, CME
VP. Sales &, Marketing
Ken-Tool 
768 E. North St.
Akron, OH  44305 
330-252-1957 office

rtysoncme@kentool.com