Ken-Tool introduces the 35359 H.D. Universal Wheel Weight Hammer

Heavier weight, ergonomic design gives greater technician efficiency

AKRON, Ohio (June 3, 2014) -- Ken-Tool, known worldwide as a leader in automotive and tire service tools, announces the release of its Heavy Duty Universal Wheel Weight Hammer (pn 35359).  The new hammer is designed for installing and removing clip-on wheel weights for light to heavy duty trucks.

The hammer is 12-in. (30.5 cm) long and features a 2.5 lb (28 oz/794 g) cast steel head -- nearly twice as heavy as comparable wheel weight hammers.  It has a non-marring, replaceable polyvinyl strike face that is 1.50 in. (3.8 cm) in diameter, which is 34% larger strike area than a typical 7/8-in. diameter hammer.  The hammer's greater mass and large strike face allows a technician to efficiently install the wheel weight with a single blow.

The fiberglass handle uses a shock resistant, ergonomic design to provide technician comfort with or without gloves, and to reduce fatigue.  It is designed for use in a heavy duty commercial environment with a rubber grip which resists common shop chemicals.  It is four times stronger than a typical wooden handle, with improved longevity.

The Ken-Tool 35359 H.D. Universal Wheel Weight Hammer works with all types of clip-on wheel weights -- lead, zinc and steel.  The mar-free strike face protects the surface of aluminum wheels, as well as chrome plated steel wheels, from damage caused by an errant hammer strike.

Also available is a Heavy Duty Universal Wheel Weight Hammer Refurbish Kit (pn 35360). The kit includes a new anti-marring impact face, chomoly steel hook, hook set screw, and hex-key wrench.

Ken-Tool products are available through leading tire industry supply distributors worldwide.  For more information about Ken-Tool’s line of professional tire-changing tools, visit www.kentool.com.  High resolution images of the 35359 H.D. Universal Wheel Weight Hammer are available on line at http://www.kentool.com/kentoolmedia_images.html.

About Ken-Tool
Ken-Tool is the world’s leading manufacturer of professional automotive and tire service tools. Headquartered in Akron, Ohio, Ken-Tool has been providing the tire industry and automotive aftermarket with quality products for over 90 years.

Contact:

Rock Tyson, CME
VP, Sales & Marketing
Ken-Tool 
Tel.:  (330) 252-1957

Email: rtysoncme@kentool.com